## Slide 1: Saturation Accumulator
Lab 01

## Slide 2: Purpose of this lab
to refresh your hardware knowledge
learn how to use the EDA tools
  try the coding style
establish your feeling on
  path delay
  chip area

## Slide 3: Spec of the accumulator
reset: clear the accumulator content (dout=0)
enable: accumulate incoming value (din) if enable=1
accumulate and saturation:
  temp = ACC+din
  if (temp>0xff) ACC=0xff;
  else ACC = temp;
SACC
1
enable
1
reset
din
8
dout
8

## Slide 4: Requirements
RTL coding in Verilog or VHDL
do logic synthesis for SAED 32-nm process and report
  timing (longest path delay)
  chip area

## Slide 5: Upload data for this lab
power-point slides including
  block-diagram design
  critical-path analysis and discussion along with the block-diagram design
  various coding style you tried to reduce chip area (discussion)
source code
simulation waveform
synthesis report

## Slide 6: Remark: How coding style affects chip area
try this code
  always @(*) begin
    out = (sel)? a+b: a-b;
  end
Add/Sub
a
b
sel
a+b
a+(~b)+1
MUX