## Slide 1: Carry Lookahead as Parallel Prefix Sum
Lecture 03 (Part F)

## Slide 2: Recap: carry lookahead adder

## Slide 3: The core problem
Q: How to design a fast n-bit adder?
  attach the O(n) carry-chain delay

## Slide 4: Framework of CLA
CLA: carry-lookahead adder for X+Y
FA
FA
FA
FA
FA
…
lookahead carry generator
pg
pg
pg
pg
pg

## Slide 5: Framework of CLA
CLA: carry-lookahead adder for X+Y
FA
FA
FA
FA
FA
…
lookahead carry generator
pg
pg
pg
pg
pg
0
0
0
1
1
0
1
1
0
1
0
0
0
1
0
1
1
0

## Slide 6: Framework of CLA
CLA: carry-lookahead adder for X+Y
FA
FA
FA
FA
FA
…
lookahead carry generator
pg
pg
pg
pg
pg
to implement Boolean equations

## Slide 7: Framework of CLA
CLA: carry-lookahead adder for X+Y
FA
FA
FA
FA
FA
…
lookahead carry generator
pg
pg
pg
pg
pg
full adders to get the sum without O(n) carry chain

## Slide 8: 4-bit look-ahead carry generation
Fig. 6.1 Four-bit carry network with full lookahead.
Full carry lookahead is quite practical for a 4-bit adder
c1 = g0  c0 p0
c2 = g1  g0 p1  c0 p0 p1
c3 = g2  g1 p2  g0 p1 p2  c0 p0 p1 p2
c4 = g3  g2 p3  g1 p2 p3  g0 p1 p2 p3
 c0 p0 p1 p2 p3

## Slide 9: Question
Q: How to design a general n-bit adder?
  brute-force Boolean equation expansion?
  the large fan-in problem
Schemes for n-bit lookahead carry generation
  Sec 6.2: hierarchical construction of lookahead carry generator
  Sec 6.3: parallel prefix computation

## Slide 10: General n-bit carry lookahead
32-input AND
Consider a 32-bit adder
c1 = g0  c0 p0
c2 = g1  g0 p1  c0 p0 p1
c3 = g2  g1 p2  g0 p1 p2  c0 p0 p1 p2
.
.
.
c31 = g30  g29 p30  g28 p29 p30  g27 p28 p29 p30  . . .  c0 p0 p1 p2 p3 ... p29 p30
32-input OR
. . .
High fan-ins necessitate tree-structured circuits

## Slide 11: Today’s Goal
carry-lookahead generator in delay O(log n)
  hierarchical design (we’ve already seen)
  as parallel prefix sum (new)

## Slide 12: Rewrite carry-lookahead as prefix sum
algebraic technique

## Slide 13: Notation on signals
g[i,j]=1 if carry is generated by x[i:j]+y[i:j]
p[i,j]=1 if carry is propagated through x[i:j]+y[i:j]

## Slide 14: Question
Q: How to generate all of the following signals as fast as possible?
  g[0,1] & p[0,1]
  g[0,2] & p[0,2]
  g[0,3] & p[0,3]
  ...
The carry:
1 0 1 1
0 1 1 1
+)

## Slide 15: The recurrence relation
Q: can you explain the intuitive meaning?

## Slide 16: The operator
(g, p)
(g", p") (g', p')
¢
g = g" + g'p"
p = p'p"

## Slide 17: Compute generate and propagate signal as prefix sum
(g, p)
(g", p") (g', p')
¢
g = g" + g'p"
p = p'p"
¢
¢
¢

## Slide 18: Example Prefix-Based Carry Network
g0, p0
g1, p1
g2, p2
g3, p3
g[0,0], p[0,0]
= (c1, --)
g[0,1], p[0,1]
= (c2, --)
g[0,2], p[0,2]
= (c3, --)
g[0,3], p[0,3]
= (c4, --)
+
+
+
+
2
6
5
-1
7
12
5
6
g0, p0
g1, p1
g2, p2
g3, p3
g[0,0], p[0,0]
= (c1, --)
g[0,1], p[0,1]
= (c2, --)
g[0,2], p[0,2]
= (c3, --)
g[0,3], p[0,3]
= (c4, --)
¢
¢
¢
¢
Four-input
prefix sums
network
Scan order
Four-bit
Carry lookahead network

## Slide 19: Criteria that you can do it as prefix sum
the operator is associative
prove by yourself
(g, p)
(g", p") (g', p')
¢
g = g" + g'p"
p = p'p"

## Slide 20: How to do this efficiently?
prefix sum in O(log n)
x0
x1
x2
x3
x4
x0
x0+x1
x0+x1+x2
x0+x1+x2+x3
x0+x1+x2+x3+x4
...
...

## Slide 21: Brent-Kung Graph
for parallel prefix sum in O(log n) delay

## Slide 22: Strategy to construct parallel prefix
divide-and-conquer
Fig. 6.8 Parallel prefix sums network built of one k/2-input network and k – 1 adders.

## Slide 23: How to construct?
Suppose you have:
  x0+x1
  x0+x1+x2+x3
  x0+x1+x2+x3+x4+x5
  x0+x1+x2+x3+x4+x5+x6+x7
How to build the following?
  x0+x1+x2
  x0+x1+x2+x3+x4
  x0+x1+x2+x3+x4+x5+x6
+
x0
x1
+
x2
x3
+
x4
x5
+
x6
x7
prefix sum for 4 numbers
x0+x1
x0+...+x3
x0+...+x5
x0+...+x7

## Slide 24: How to construct?
Suppose you have:
  x0+x1
  x0+x1+x2+x3
  x0+x1+x2+x3+x4+x5
  x0+x1+x2+x3+x4+x5+x6+x7
How to build the following?
  x0+x1+x2
  x0+x1+x2+x3+x4
  x0+x1+x2+x3+x4+x5+x6
+
x0
x1
+
x2
x3
+
x4
x5
+
x6
x7
prefix sum for 4 numbers
x0+x1
x0+...+x3
x0+...+x5
x0+...+x7
+
x0+x1+x2

## Slide 25: How to construct?
Suppose you have:
  x0+x1
  x0+x1+x2+x3
  x0+x1+x2+x3+x4+x5
  x0+x1+x2+x3+x4+x5+x6+x7
How to build the following?
  x0+x1+x2
  x0+x1+x2+x3+x4
  x0+x1+x2+x3+x4+x5+x6
+
x0
x1
+
x2
x3
+
x4
x5
+
x6
x7
prefix sum for 4 numbers
x0+x1
x0+...+x3
x0+...+x5
x0+...+x7
+
x0+x1+x2+x3+x4

## Slide 26: Rule of the Thumb
divide-and-conquer
Fig. 6.8 Parallel prefix sums network built of one k/2-input network and k – 1 adders.

## Slide 27: Rule of the Thumb
divide-and-conquer
Fig. 6.8 Parallel prefix sums network built of one k/2-input network and k – 1 adders.
odd-even
bypass
even-odd

## Slide 28: Brent-Kung Graph for 16 numbers
Fig. 6.9 Brent-Kung parallel prefix graph for
16 inputs.

## Slide 29: Brent-Kung Graph for 16 numbers
Fig. 6.9 Brent-Kung parallel prefix graph for
16 inputs.
prefix sum for 8 numbers

## Slide 30: Brent-Kung Graph for 16 numbers
Fig. 6.9 Brent-Kung parallel prefix graph for
16 inputs.
prefix sum for 4 numbers

## Slide 31: Kogge-Stone Graph
parallel prefix sum with delay O(log n)

## Slide 32: Strategy to build parallel prefix
Stage 1: generate sums of 2 consecutive numbers
  x0+x1,
  x1+x2,
  x2+x3,
  x3+x4,...
Stage 2: generate sums of 4 consecutive numbers
  x0+x1+x2+x3,
  x1+x2+x3+x4,
  x2+x3+x4+x5,...
Stage 3: generate sums of 8 consecutive numbers
Stage 4: generate sums of 16 consecutive numbers
...

## Slide 33: How to build?
Suppose: we have sums of 2 consecutive numbers
  x0+x1, x1+x2, x2+x3,...
Want to Compute: sums of 4 consecutive numbers
  x0+x1+x2+x3, x1+x2+x3+x4, ...
x0
x1
x2
x3
x4
x5
x6
x7
x0
x0+x1
x1+x2
x2+x3
x3+x4
x4+x5
x5+x6
x6+x7
+
x0+x1+x2+x3
+
x1+x2+x3+x4
+
x2+x3+x4+x5
...
gap of 2

## Slide 34: Strategy to build parallel prefix
Stage 1: generate sums of 2 consecutive numbers
  x0+x1, x1+x2, x2+x3, x3+x4,...
Stage 2: generate sums of 4 consecutive numbers
  x0+x1+x2+x3, x1+x2+x3+x4, x2+x3+x4+x5,...
Stage 3: generate sums of 8 consecutive numbers
Stage 4: generate sums of 16 consecutive numbers
...

## Slide 35: Strategy to build parallel prefix
Stage 1: generate sums of 2 consecutive numbers
  x0+x1, x1+x2, x2+x3, x3+x4,...
Stage 2: generate sums of 4 consecutive numbers
  x0+x1+x2+x3, x1+x2+x3+x4, x2+x3+x4+x5,...
Stage 3: generate sums of 8 consecutive numbers
Stage 4: generate sums of 16 consecutive numbers
...
x0+x1
x1+x2

## Slide 36: Strategy to build parallel prefix
Stage 1: generate sums of 2 consecutive numbers
  x0+x1, x1+x2, x2+x3, x3+x4,...
Stage 2: generate sums of 4 consecutive numbers
  x0+x1+x2+x3, x1+x2+x3+x4, x2+x3+x4+x5,...
Stage 3: generate sums of 8 consecutive numbers
Stage 4: generate sums of 16 consecutive numbers
...

## Slide 37: Strategy to build parallel prefix
Stage 1: generate sums of 2 consecutive numbers
  x0+x1, x1+x2, x2+x3, x3+x4,...
Stage 2: generate sums of 4 consecutive numbers
  x0+x1+x2+x3, x1+x2+x3+x4, x2+x3+x4+x5,...
Stage 3: generate sums of 8 consecutive numbers
Stage 4: generate sums of 16 consecutive numbers
...
x0+x1+x2+x3

## Slide 38: Strategy to build parallel prefix
Stage 1: generate sums of 2 consecutive numbers
  x0+x1, x1+x2, x2+x3, x3+x4,...
Stage 2: generate sums of 4 consecutive numbers
  x0+x1+x2+x3, x1+x2+x3+x4, x2+x3+x4+x5,...
Stage 3: generate sums of 8 consecutive numbers
Stage 4: generate sums of 16 consecutive numbers
...
x1+x2+x3+x4

## Slide 39: More on parallel prefix sum
F. Thompson Leighton, Introduction to Parallel Algorithms and Architectures: Arrays, Trees, and Hypercubes

## Slide 40: Wakeup!
How to realize carry lookahead generator with the architecture?
  what’s xis?
  the operator in each node?