## Slide 1: Residue Number System
to demonstrate how number encoding may result in fast hardware
Lecture 02 (Part E)

## Slide 2: The Motivating Problem
Objective: to design a fast adder
  with critical path as short as possible

## Slide 3: Critical path analysis for the adder

## Slide 4: How a computer performs binary addition
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}
0 1 1 0
0 0 1 1
+)
A
B
S

## Slide 5: How a computer performs binary addition
Step 1: addition for bit 0
0 1 1 0
0 0 1 1
+)
A
B
S
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}

## Slide 6: How a computer performs binary addition
Step 1: addition for bit 0
0 1 1 0
0 0 1 1
+)
A
B
S
1
0
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}
Carry C[1]
Sum S[0]

## Slide 7: How a computer performs binary addition
Step 2: addition for bit 1 with carry
0 1 1 0
0 0 1 1
+)
A
B
S
1
0
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}

## Slide 8: How a computer performs binary addition
Step 2: addition for bit 1 with carry
0 1 1 0
0 0 1 1
+)
A
B
S
1
0
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}
0
1

## Slide 9: How a computer performs binary addition
Step 2: addition for bit 1 with carry
0 1 1 0
0 0 1 1
+)
A
B
S
1
0
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}
0
1
0
Carry C[2]
Sum S[1]

## Slide 10: How a computer performs binary addition
repeat the procedure and we get the result
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}
0 1 1 0
0 0 1 1
+)
A
B
S
1 0 0 1
So, what’s the basic cell for the addition?

## Slide 11: Full Adder: the basic component for an adder
a combinational circuit doing the following truth table
to perform addition for a bit i
FA
X
Y
S
Cin
Cout
0
0
0
0
0
0
0
1
0
1
0
1
0
0
1
0
1
1
1
0
1
0
0
0
1
1
0
1
1
0
1
1
0
1
0
1
1
1
1
1
X
Y
Cin
Cout
S
0 1 1 0
0 0 1 1
+)
A
B
S
1
0
0
1

## Slide 12: Carry-Propagation Adder
FA
FA
FA
FA
FA
…
A[0]
B[0]
A[1]
B[1]
A[2]
B[2]
A[n-2]
B[n-2]
A[n-1]
B[n-1]
S[0]
S[1]
S[2]
S[n-2]
S[n-1]
Cin
Cout
Adder
n
A
n
B
n
S
Cin
Cout
always @(*)
{Cout, S} = A+B+Cin;

## Slide 13: Critical path analysis
critical path for n-bit adder: O(n)
FA
FA
FA
FA
FA
…
A[0]
B[0]
A[1]
B[1]
A[2]
B[2]
A[n-2]
B[n-2]
A[n-1]
B[n-1]
S[0]
S[1]
S[2]
S[n-2]
S[n-1]
Cin
Cout

## Slide 14: Core problem of fast adder design
How to reduce the O(n) critical path
residue number system (RNS) provides a way to “segment” the O(n) carry-chain

## Slide 15: Strategy of RNS for fast adder design
transform scalar operation to be vector operation
  operate on vectors with smaller number
Example: RNS with primes {3,5,7}
+)
+)

## Slide 16: Chinese remainder theorem – first visit
ad-hoc solution from ancient Chinese

## Slide 17: The motivating problem
孫子算經:
  今有物不知其數，三三數之剩二，五五數之剩三，七七數之剩二，問物幾何？
Find an integer x such that
  x mod 3 = 2
  x mod 5 = 3
  x mod 7 = 2
Answer: x=23+3*5*7*k

## Slide 18: Solution strategy
simplify, simplify, and simplify,…
a simpler version of this problem:
  find an integer x such that
    for some integer q1 and q2

## Slide 19: Roadmap for further simplify
Problem: find integer x such that
Problem: find integer x such that
Problem: find integer x such that

## Slide 20: Simplified Problem (2)
Problem: find integer x such that
The trial:
  5, 10, 15, 20, 25, …
Observation: gap btw/ two solutions=15

## Slide 21: Simplified Problem (2)
Problem: find integer x such that
The trial:
  3, 6, 9, 12, 15, 18, 21, 24, …
Observation: gap btw/ two solutions=15

## Slide 22: Roadmap for further simplify
Problem: find integer x such that
Problem: find integer x such that
Problem: find integer x such that
solved!

## Slide 23: Simplified Problem (1)
Problem:
  Given integer x0: solution to
  Want to Find: integer x such that
    from x0

## Slide 24: Simplified Problem (1)
Analysis:
  x0=10 is a solution to
  let’s check the real-line:
  x = 2*x0 = 20 is a solution to
0
10
3q1
1
10
3q1
1

## Slide 25: Simplified Problem (1)
Analysis:
  x0=6 is a solution to
  the real-line:
  x = 3*x0 = 18 is a solution to
0
6
5q2
1
6
5q2
1
6
5q2
1

## Slide 26: Simplified Problem (1)
General scheme:
  Let x0 be a solution to
  Then x= x0*r is a solution to
Justify:

## Slide 27: Simplified target problem
Problem:
  Given:
    x0: solution to
    x1: solution to
  Want to Find: integer x such that

## Slide 28: Simplified target problem
We have
  x0=20 is a solution to
  x1=18 is a solution to
Let x=x0+x1=20+18=38 and observe the real-line
20
3q1
2
5q2
18
3q’1
5q’2
3

## Slide 29: Simplified target problem
Let x=x0+x1=20+18=38 and observe the real-line
20
3q1
2
5q2
18
3q’1
5q’2
3
20
3q1
2
5q2
18
3q’1
5q’2
3

## Slide 30: Simplified target problem
General scheme:
  Let x0: solution to
  Let x1: solution to
  Then x= x0 + x1 is a solution to
Justify:

## Slide 31: Simplified target problem
Observation: the solution appears with gap 3*5=15
  solutions: 8, 23, 38, 53, 68, …
Why? Justify

## Slide 32: In-Class Exercise
Problem: find an integer x such that
  for some integers q1, q2, and q3

## Slide 33: Chinese remainder theorem revisited
from the view point of modern algebra

## Slide 34: Chinese Remainder Theorem
Zk={0, 1, 2, …, k-1}
How to prove it?
  Hint: quotient ring theory in abstract algebra
  see Herstein, Abstract Algebra

## Slide 35: Example of CRT
Problem: find an integer x between 0 and 104 such that
Answer: x=23
Q: Can you find another x between 0 to 104?
Note: 3, 5, 7 are all primes!

## Slide 36: Residue Number System

## Slide 37: Example of RNS
fix the set of primes {3, 5, 7}
we denote
23 is the unique x in [0, 104] such that

## Slide 38: In-Class Exercise
represent the numbers in RNS with base (3,5,7)
  47 = (?, ?, ?)
  15 = (?, ?, ?)
  68 = (?, ?, ?)

## Slide 39: Why we want RNS
to design a fast adder
algebra to operate the vectors (a, b, c)RNS

## Slide 40: Algebra of RNS

## Slide 41: Example: RNS addition
Consider: RNS with {3, 5, 7}
23=(2, 3, 2)RNS
19=(1, 4, 5)RNS
Justify: 42=(0, 2, 0)
  23 = 3*7+2
  19 = 3*6+1
  23+19 = 3*(7+6)+3 = 3*(7+6) + 3*1+0

## Slide 42: Addition for RNS

## Slide 43: Proof of addition for RNS

## Slide 44: In-Class Exercise
RNS addition with base (3, 5, 7)
  17+32
  25+36
  19+15

## Slide 45: Algebra of RNS
Prove subtraction and multiply
by yourself

## Slide 46: Example: RNS multiply
Consider: RNS with primes {3, 5, 7}
Justify:
  23=5*4+3
  23*4=5*4*4+3*4=5*16+12=5*16+5*2+2

## Slide 47: Put it all together
compare the ad-hoc solution and linear algebra approach

## Slide 48: Example
Problem: find integer x such that
Problem:
  Consider RNS with primes {3, 5, 7}
  Find:

## Slide 49: General scheme with example (2,3,2)RNS
RNS with primes{3,5,7}
setup unit vectors
find value for each coordinate
take sum for all coordinates

## Slide 50: In-Class Exercise
Problem: find integer x such that
Problem:
  Consider RNS with primes {3, 5, 7}
  Find:

## Slide 51: RNS Adder

## Slide 52: Basic scheme of RNS adder
doing operation on vectors with smaller numbers
Example: RNS with primes {3,5,7}
+)
+)

## Slide 53: Example: an adder for RNS
with primes {3,5,7,8}
Fig. 4.2 The structure of an adder, subtractor, or multiplier for RNS(8|7|5|3).
Fig. 4.1 Binary-coded format for RNS(8 | 7 | 5 | 3).

## Slide 54: Example: an adder for RNS
with primes {3,5,7,8}
Fig. 4.2 The structure of an adder, subtractor, or multiplier for RNS(8|7|5|3).
Fig. 4.1 Binary-coded format for RNS(8 | 7 | 5 | 3).
dedicated truth-table
doing (a+b) mod 7

## Slide 55: Problems Remaining
How to convert RNS back to binary encoding?
  with small hardware
How to do complex arithmetic?
  multiply, division
  compare >, <, == (see Example 4.3 at page 65)
RNS is usually for signal processing, not individual scalar operation!

## Slide 56: Homework #2
Prove the multiplication rule of RNS

## Slide 57: HW#2: Problem Description
Consider: an RNS formed by co-prime numbers (n1, n2, …, nk-1)
Let x and y be two integers in the range of the RNS
Suppose x*y is still in the range of the RNS
Prove: