## Slide 1: Synthesizable Verilog Coding
review of preliminary knowledge
Lecture 01 (Part D)

## Slide 2: Outline
synthesizable Verilog coding
  overview
  structural description
  behavior description: combinational vs. sequential circuit
simulation support
Lab 01

## Slide 3: State-of-art chip design
RTL design
(Register Transfer Level)
gate-level design
circuit-level design
(transistor-level)
physical layout
always @(posedge clk)
A <= B+C;
automatically
processed by EDA
tools

## Slide 4: Common error of beginners
non-synthesizable coding style
  a wrong code may result in correct simulation wave-form/FPGA outcome
synthesizable but without concrete imagine on hardware generated
  long path delay
  extremely large chip area

## Slide 5: Caution

## Slide 6: Correct method of doing RTL coding
Step 1: draw the block diagram of your hardware
  be aware of combinational and sequential circuit
Step 2: translate each block into Verilog/VHDL code
  follow fixed coding style

## Slide 7: Verilog coding
structural description
  describe the hardware directly
behavior description
  most of beginners error

## Slide 8: Structural description

## Slide 9: Example of structural description

## Slide 10: Example of structural description
input/output specification

## Slide 11: Example of structural description

## Slide 12: Example of structural description

## Slide 13: Instance Sub-Modules

## Slide 14: Hierarchical modules

## Slide 15: Instance name of a module

## Slide 16: Declare wires

## Slide 17: Connecting ports of modules

## Slide 18: Caution
always use “wire” to declare signals in structural description
no “always @(…)” in structural description

## Slide 19: Behavior description

## Slide 20: What is behavior description
declare with “reg”
  although some may be synthesized as wires
use “always @(…)” to describe the “rule to generate output”
  not a step-by-step executing program

## Slide 21: Caution on behavior description
Be aware of which part is combinational circuit and which part is sequential circuit
use fixed coding style for
  combinational circuit
  sequential circuit
Do not try other coding styles!

## Slide 22: Inferring combinational circuit with behavior description

## Slide 23: The general scheme
for combinational circuit
hardware to be
simulated
A
B
C
D
E
always @(A or B or C) begin
…
// C code to compute D and E
…
end

## Slide 24: Inferring combinational circuit
general coding style:
  always @(all signal list)
  always @(*)
  use blocking assignment “=“
    do not use “<= “
  you have to enumerate all cases to determine the output value

## Slide 25: Example 1: combinational circuit

## Slide 26: Example 1: combinational circuit
register is not a register!

## Slide 27: Example 1: combinational circuit
C-like code to compute output from inputs

## Slide 28: Example 1: combinational circuit
specify a don’t-care

## Slide 29: Example 1: combinational circuit
if-then-else rules also work!

## Slide 30: Example 1: combinational circuit
This line is necessary to enforce
a combinational circuit

## Slide 31: Example 1: combinational circuit
Verilog 2001 standard:
depends on all input signals

## Slide 32: Inferring sequential circuit with behavior description

## Slide 33: The general scheme
for sequential circuit
  only simulate when clock triggered
hardware to be
simulated
A
B
C
D
E
always @(posedge clk) begin
…
// C code to compute D and E
…
end
clk

## Slide 34: Inferring sequential circuit
coding style:
  always @(posedge clk)
  use non-blocking assignment “<=“

## Slide 35: Example 2: sequential circuit
parallel D-FFs triggered by clock

## Slide 36: Example 2: sequential circuit
parallel D-FFs triggered by clock
simulation triggered by clock

## Slide 37: Example 2: sequential circuit
parallel D-FFs triggered by clock
Caution: You have to use non-blocking assignment
to generate registers!

## Slide 38: Example 3: sequential circuit
with combinational circuit for computation

## Slide 39
I believe that most of you are confused with
  combinational circuit vs.
  sequential circuit

## Slide 40: Example: the adder
combinational vs. sequential circuit

## Slide 41: What’s the difference?
reg [3:0] A, B, C;
always @(*) begin
A = B+C;
end
reg [3:0] A, B, C;
always @(posedge clk) begin
A <= B+C;
end

## Slide 42: What’s the difference?
reg [3:0] A, B, C;
always @(*) begin
A = B+C;
end
reg [3:0] A, B, C;
always @(posedge clk) begin
A <= B+C;
end
+
B
C
A
+
B
C
A
clk
register

## Slide 43: What’s the difference?
reg [3:0] A, B, C;
always @(*) begin
A = B+C;
end
reg [3:0] A, B, C;
always @(posedge clk) begin
A <= B+C;
end
10
5
15
1
2
3
5
7
12
B
C
A
clk
10
5
15
1
2
3
5
7
12
B
C
A
clk

## Slide 44: Simulation Support
code only for simulation, not to synthesize real hardware

## Slide 45: General guidelines to coding for simulation support
in behavior descriptions only
event-driven programming and coding like C
system tasks to display results or dump waveform
Example:
  to dump the content of “out” signals every cycle
    always @(posedge clk) begin
      #2; //delay 2 units of simulation time
      $display (“out = %h”, out);
    end

## Slide 46: Sample code for simulation support
to generate the clock signal
  initial clk=0;
  always #5 clk=~clk;
clk
5 unit
5 unit

## Slide 47: Sample code for simulation support
to feed test patterns
Hardware you
designed
din1
din2
0
1
2
3
0xa
0x2
0x5
0x4
0x9
0x5
don’t-care
don’t-care
sim_cycle
din1
din2
time

## Slide 48: Dump waveforms
IEEE standard waveform format (.vcd)
  specify the file name of the waveform:
    $dumpfile (“file_name”)
  specify the scope of signals to dump:
    $dumpvars (scope_and_signal_name);
  start waveform dumping:
    $dumpon;
  stop waveform dumping:
    $dumpoff;

## Slide 49: Dump waveforms
Synopsys supported format (VPD+)
  specify the file name
    $vcdplusfile (“filename”);
  start dumping and specify the scope:
    $vcdpluson (scope_and_signals_name);
  stop dumping:
    $vcdplusoff;

## Slide 50: More on simulation support
specify the timescale
call a complete task
call a C function
  Verilog standard: PLI (Programming Language Interface)
  Synopsys special: direct-C
Please check-out the manual!