## Slide 1: Division Overview
Lecture 05 (Part A)

## Slide 2: Today’s Content
Recap: basic division scheme
Strategy to design fast division
  write as recurrence relation
basic division scheme revisited: as recurrence relation
non-restoring division: as recurrence relation

## Slide 3: Recap: basic division scheme

## Slide 4: How the hardware performs division
Again, the method you learned in elementary school, but in binary
Example: 117/10
  117 = 0111 0101
  10 = 1010

## Slide 5: Basic division scheme
Notation for our discussion of division algorithms:
z Dividend z2k–1z2k–2 . . . z3z2z1z0
d Divisor dk–1dk–2 . . . d1d0
q Quotient qk–1qk–2 . . . q1q0
s Remainder, z – (d  q) sk–1sk–2 . . . s1s0
Initially, we assume unsigned operands
Fig. 13.1 Division of an 8-bit number by a 4-bit number in dot notation.

## Slide 6: Divider hardware you learned before
Fig. 13.5 Shift/subtract sequential restoring divider.

## Slide 7: How to do fast division?

## Slide 8: Difficulties to do division
Division is more complex than multiplication:
Need for quotient digit selection or estimation
Overflow possibility: the high-order k bits of z
must be strictly less than d; this overflow check
also detects the divide-by-zero condition.
Pentium III latencies
Instruction Latency Cycles/Issue
Load / Store 3 1
Integer Multiply 4 1
Integer Divide 36 36
Double/Single FP Multiply 5 2
Double/Single FP Add 3 1
Double/Single FP Divide 38 38

## Slide 9: How we achieve fast division
high-radix division: deals with multiple bits in each step
guess the quotient bits and compensate (if error) at the next step
formulate as recurrence relation!
Fig. 14.1
Radix-4 division in dot notation

## Slide 10: Basic division scheme revisited
formulate as recurrence relation

## Slide 11: The recurrence relation
Given:
  z: dividend (2k-bit integer)
  d: divior (k-bit integer)
  (to do z/d)
Initialization:
Inductive Step:
Result: the bit vector (q-1, q-2, ..., q-k) is the quotient and s(k) is the remainder

## Slide 12: In-class Exercise
Do the division 117/10 with the recurrence relation
  117 = 0111 0101
  10 = 1010

## Slide 13: Example of basic division

## Slide 14: Division recurrence
Division with left shifts
s(j) = 2s(j–1) – qk–j (2k d) with s(0) = z and
|–shift–| s(k) = 2ks
|––– subtract –––|
(There is no corresponding right-shift algorithm)
Fig. 13.1
k bits
k bits
2z
2k d
0

## Slide 15: Difficulty with the recurrence relation
Needs comparison to determine q-j

## Slide 16: Non-restoring division as recurrence relation

## Slide 17: Key Idea of the derivation
representing partial products in radix-2 number system with range [-1,1]

## Slide 18: Radix-2 with range [-1,1]
Example:
  (-1, 1, 0, -1, 1, 0) representing

## Slide 19: The recurrence relation for non-restoring division
Given:
  z: dividend (2k-bit integer)
  d: divior (k-bit integer)
  (to do z/d)
Initialization:
Inductive Step:
Result: the bit vector (q-1, q-2, ..., q-k) is the quotient and s(k) is the remainder

## Slide 20: In-class Exercise
Do the division 117/10 with the recurrence relation
  117 = 0111 0101
  10 = 1010

## Slide 21: In-Class Exercise
convert the vector to 2’s completement representation
  (1, 1, -1, 1)

## Slide 22: Quotient conversion scheme
1 1 -1 1
1 1 0 1
-1 -1 -1 -1
+)
1 1 0 1
+)
-1
1

## Slide 23: Quotient conversion scheme
1 1 -1 1
1 1 0 1
-1 -1 -1 -1
+)
1 1 0 1
+)
-1
1

## Slide 24: Quotient conversion scheme
1 1 -1 1
1 1 0 1
-1 -1 -1 -1
+)
1 1 0 1
+)
-1
1

## Slide 25: Question
How to implement non-restoring division?
  no -1
The rule to set quotient digit:
correct the quotient at final

## Slide 26: In-Class Exercise
perform 117/10 in the implementation scheme