## Slide 1: Overview on Adder Design
things you learned and not learned on digital circuit course
Lecture 03 (Part A)

## Slide 2: Basic adder design
the adder you learned in digital circuit course

## Slide 3: How a computer performs binary addition
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}
0 1 1 0
0 0 1 1
+)
A
B
S

## Slide 4: How a computer performs binary addition
Step 1: addition for bit 0
0 1 1 0
0 0 1 1
+)
A
B
S
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}

## Slide 5: How a computer performs binary addition
Step 1: addition for bit 0
0 1 1 0
0 0 1 1
+)
A
B
S
1
0
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}
Carry C[1]
Sum S[0]

## Slide 6: How a computer performs binary addition
Step 2: addition for bit 1 with carry
0 1 1 0
0 0 1 1
+)
A
B
S
1
0
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}

## Slide 7: How a computer performs binary addition
Step 2: addition for bit 1 with carry
0 1 1 0
0 0 1 1
+)
A
B
S
1
0
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}
0
1

## Slide 8: How a computer performs binary addition
Step 2: addition for bit 1 with carry
0 1 1 0
0 0 1 1
+)
A
B
S
1
0
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}
0
1
0
Carry C[2]
Sum S[1]

## Slide 9: How a computer performs binary addition
repeat the procedure and we get the result
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}
0 1 1 0
0 0 1 1
+)
A
B
S
1 0 0 1
So, what’s the basic cell for the addition?

## Slide 10: Full Adder: the basic component for an adder
a combinational circuit doing the following truth table
to perform addition for a bit i
FA
X
Y
S
Cin
Cout
0
0
0
0
0
0
0
1
0
1
0
1
0
0
1
0
1
1
1
0
1
0
0
0
1
1
0
1
1
0
1
1
0
1
0
1
1
1
1
1
X
Y
Cin
Cout
S
0 1 1 0
0 0 1 1
+)
A
B
S
1
0
0
1

## Slide 11: Ripple-Carry Adder
FA
FA
FA
FA
FA
…
A[0]
B[0]
A[1]
B[1]
A[2]
B[2]
A[n-2]
B[n-2]
A[n-1]
B[n-1]
S[0]
S[1]
S[2]
S[n-2]
S[n-1]
Cin
Cout
Adder
n
A
n
B
n
S
Cin
Cout
always @(*)
{Cout, S} = A+B+Cin;
0 1 1 0
0 0 1 1
+)
A
B
S
1 0 0 1

## Slide 12: Full-adder implementation
Fig. 5.2 (alternate version) Possible designs for a full-adder in terms of half-adders, logic gates, and CMOS transmission gates.

## Slide 13: How to generate flags for signed number addition
things you learned in digital circuit course by may be unfamiliar

## Slide 14: Representing a signed number
the 2’s complement representation
Examples:
  (0101)=5
  (1011)=-5
    ~(0101)+1

## Slide 15: Flags for signed number addition
carry-out
overflow OF:
negative N:
zero Z:

## Slide 16: Signed adder with flag generation
Fig. 5.7 Two’s-complement adder with provisions for detecting conditions and exceptions.

## Slide 17: Signed adder with flag generation
Fig. 5.7 Two’s-complement adder with provisions for detecting conditions and exceptions.
Carry-out

## Slide 18: Signed adder with flag generation
Check the most significant bit for the sign of the result

## Slide 19: Signed adder with flag generation
The result is 0 if every bit is 0

## Slide 20: Signed adder with flag generation
I believe you have difficulty to derive this!

## Slide 21: In-Class Exercise
Derive the rule:
Hint: start from the vector representation of a signed number
  The case that the highest element is outside the range {-1,0}

## Slide 22: So that’s what you learned before about the adder
is it really so simple?

## Slide 23: Core Problems
design an extremely small adder
  use as few chip area as possible
design an extremely fast adder
  path-delay as short as possible
design an extremely low-power adder
  will not mentioned in this course

## Slide 24: How to do these optimized designs
check what you can do through the VLSI implementation stack
ESL design
(Electronic System Level)
RTL design
(Register Transfer Level)
gate-level design
circuit-level design
(transistor-level)
physical layout

## Slide 25: How to build a small adder
an overview

## Slide 26: How to do a small adder
a bit-serial adder
  Figure 5.3(a) at page 78
ESL design
(Electronic System Level)
RTL design
(Register Transfer Level)
gate-level design
circuit-level design
(transistor-level)
physical layout

## Slide 27: How to do a small adder
direct design of a full adder
  not composed from half-adder
ESL design
(Electronic System Level)
RTL design
(Register Transfer Level)
gate-level design
circuit-level design
(transistor-level)
physical layout

## Slide 28: How to do a small adder
take a full-adder as a cell
and optimize
ESL design
(Electronic System Level)
RTL design
(Register Transfer Level)
gate-level design
circuit-level design
(transistor-level)
physical layout

## Slide 29: Full-adder as a cell
implement this as a cell

## Slide 30: Let’s see the FA-cell provided by UMC

## Slide 31: Check the reference
Uyemura, Introduction to VLSI Circuits and Systems
  Chap. 2: logic design with MOSFET
    Sec. 2.5: Transmission gate circuits

## Slide 32: How to design a fast adder

## Slide 33: How to design a fast adder
various architectures to reduce the carry-chain
ESL design
(Electronic System Level)
RTL design
(Register Transfer Level)
gate-level design
circuit-level design
(transistor-level)
physical layout

## Slide 34: How to design a fast adder
various architectures to reduce the carry-chain
  Carry-lookahead adders
    hierarchical
    prefix computation
  Alternative adders
    carry-skip adders
    carry-select adders
ESL design
(Electronic System Level)
RTL design
(Register Transfer Level)
gate-level design
circuit-level design
(transistor-level)
physical layout

## Slide 35: How to design a fast adder
asynchronous circuit design
ESL design
(Electronic System Level)
RTL design
(Register Transfer Level)
gate-level design
circuit-level design
(transistor-level)
physical layout

## Slide 36: How to design a fast adder
Manchester carry-chain
dual-rail logic network
dynamic circuit
ESL design
(Electronic System Level)
RTL design
(Register Transfer Level)
gate-level design
circuit-level design
(transistor-level)
physical layout

## Slide 37: Reference: a fast full-adder with circuit-level optimization
Uyemura, Introduction to VLSI Circuits and Systems
  Sec. 12.1: full-adder with dual-rail logic network